## Slide 1: National Traffic System (NTS) An Introduction

## Slide 2: MESSAGES
Should be
  CLEAR
  CONCISE
  BRIEF…and to the point!

## Slide 3: POOR TRAFFIC HANDLING

## Slide 4: What is the National Traffic System (NTS)?
The “RELAY” in American Radio Relay League (ARRL)
Started in 1915 as the formal ARRL system to relay messages around the country
Transmit & Receive Modes: Voice, CW, Digital
NTS and Amateur Radio Emergency Services (ARES)
Requirements to join: Any level license & desire to serve
ARRL Field Organization Appointments: Official Relay Station (ORS), Digital Relay Station (DRS) & Section Traffic Manager (STM).

## Slide 5: Advantages of NTS Messaging
Wireless! Send them from anywhere.
Use a little HT or a big base station
Standard Format
Accountability
NTS Nets meet daily
Can send by phone, CW or digital
When all else fails…
Fun, good practice & helpful!

## Slide 6: NTS Hierarchy and Modes
US and Canada organized into Area, Region, and Local Nets
  3 Areas
  12 Regions
Traffic Flow:
Section/ Local Nets
Region Nets
Area Nets
Area Nets
TCC
Region Nets
Section / Local Nets
VHF/UHF Phone, HF Phone, CW, Digital
HF Phone, CW, Digital

## Slide 7: NTS Areas
PAN
CAN
EAN

## Slide 8: States/Provinces, Regions and Areas
State | Region | Area
CT, ME, MA, NH, RI, VE | 1RN | EAN
NJ, NY | 2RN | EAN
DE, DC, MD, PA | 3RN | EAN
FL, GA, NC, PR, SC, VI, VA | 4RN | EAN
MI, OH, WV | 8RN | EAN
LB, NB, NF, NS, ON, PE, PQ | 2RN | EAN
AL, AR, LA, MS, OK, TN, TX | 5RN | CAN
IL, IN, KY, WI | 9RN | CAN
IA, KS, MB, MN, MO, NE, ND, NWT, SK, SD | 10RN | CAN
CA, GU, HI, NV | 6RN | PAN
AK, AB, BC, ID, MT, NWT, OR, WA | 7RN | PAN
AZ, CO, NM, UT, WY | 12RN | PAN

## Slide 9: Message Format
The ARRL Radiogram

## Slide 10
704 R C N2GS 14 CHESTER NJ 1830 JUL 2
GREG SZPUNAR N2GS
JOE SMITH KC2XXY 1234 SECOND ST SUMMIT NJ 07901
650-123-4567
austin AK2US 7/2/03 2112 EDT
THIS IS THE ARRL RADIOGRAM FORM XRAY DETAIL TO FOLLOW XRAY HAVE FUN 73

## Slide 11: ARRL Radiogram Form
Preamble: Message number, precedence, HX (optional handling code), station of origin, check (text word count), place of origin, time filed (optional), and date.
Addressee: Name, call sign (if a ham), full street address, city, 2-letter state abbreviation, zip code (very important) & telephone (be sure to include area code).
This Radio Message was received at: Station identification and location.
Text: 25 words maximum, 5 per line; Use the word “xray” for a period (.) and “query” for a question mark (?). Last word in salutation (e.g., “73”, “Love”, etc.)
Signature: (Write-in above REC’D block) Name & call sign of person who wrote the message – include full phone number if not a Ham or if new to NTS.
REC’D & SENT: Record the names and call sign of the person you rec’d the message from and/or sent/forwarded the message to, along with the date & time (EST/EDT or Z).

## Slide 12: Radiogram Form Detail (1 of 6)
Number
  Assigned by the message originator
  No standard way of numbering messages
  Consecutive (1, 2, 3..., starting over at the new year or monthly)
  Order by month & number (507 = 7th you originated in May; 11244 = 244th message you originated in November
Precedence (Emergency, P, W, or R)
  Emergency (life or death urgency in a declared emergency) always spelled out
  P = Priority (official traffic in a declared emergency)
  W = Health & Welfare (used only in a declared emergency)
  R = Routine (everything else – most frequently used)
704 R C N2GS 14 CHESTER NJ 1830 JUL 2

## Slide 13: Radiogram Form Detail (2 of 6)
(Optional) HX or Handling Code – A, B, C, D, E, F or G
  Collect landline delivery authorized within ___ miles of addressee or unlimited if blank (A150 = collect call authorized w/in 150 miles; A = collect call authorized regardless of miles)
  Cancel message if not delivered within ___ hours of filing time & service originating station (B72 = cancel if not delivered within 72 hrs and send message to originator to notify them)
  Confirmation of delivery requested by originating station (“TOD YOUR 1014 JULY 4 1330 PST XRAY 73” or if issues “ARL SIXTY SEVEN 1014 PHONE 650 555 1212 INCORRECT NO REPLACEMENT FOUND SENT RADIOGRAM INSTEAD XRAY 73”
  Report your identity & time/date rec’d message plus time/date delivered or sent to another
  Delivering station to get reply from addressee and send to originator as a new message
  Hold delivery until ___ (numbered day of month) – great for birthday or anniversary messages (F14 = deliver on 14th of the month; F1 = deliver on the 1st of month after date filed)
  Delivery by mail or toll call not required, service originating station (often ignored).
704 R C N2GS 14 CHESTER NJ 1830 JUL 2

## Slide 14: Radiogram Form Detail (3 of 6)
Station of Origin: Call sign of station who put the message into NTS format; If N2GS prepares message 1207 for a fellow ham, then puts it onto an NTS packet BBS for relay to Vermont, the originator is... N2GS. If WB2W prepares message 23 for his non-ham neighbor then gives it to N2GS to relay to any NTS net, the originator is... WB2W.
Check: The word count in body text only (do not count the address or signature); precede with “ARL” if any of the ARL numbered texts are used (e.g., ARL 7).
Place of Origin: The city & state where the message was written.
(Optional) Time Filed: This is not used much... 24-hr format & time zone
Date: Month (non-numeric – abbreviated) & day number message was created e.g., Sep 21).
704 R C N2GS 14 CHESTER NJ 1830 JUL 2

## Slide 15: Radiogram Form Detail (4 of 6)
To: Name, call sign (if going to a ham), street address or P.O. Box, city, state (abbreviated) & zip code. Note: Digital and packet NTS messages are routed via zip code.
Telephone Number: Be sure to include the area code and double-check the number!!!
This Radio Message was received at: Your station identification, date received, and your location. More received-from detail will go in the “REC’D” block after body text and signature.
JOE SMITH KC2XXY 1234 SECOND ST SUMMIT NJ 07901
650-123-4567

## Slide 16: Radiogram Form Detail (5 of 6)
Text: 25 words maximum, 5 per line; Use “xray” for a period (.) and “query” for a question mark (?).
Signature: There is no “Signature” field, just write-in below text; Name & call sign of author – include phone number if not a ham or if not known on an NTS net.
THIS IS THE ARRL RADIOGRAM FORM XRAY DETAIL TO FOLLOW XRAY HAVE FUN 73
GREG SZPUNAR N2GS

## Slide 17: Radiogram Form Detail (6 of 6)
REC’D: Call sign from whom you received the message and date & time of receipt. Time may be either your local time (EST/EDT) or Zulu time. Make sure date agrees with time base. Zulu is 4 (or 5) hours ahead of EST – can cause date to roll forward.
SENT: Call sign you sent or passed the message to, or to whom you delivered it, with date & time. Also good to note delivery method for your own reference (i.e., via phone or left on Tom’s voicemail). Always leave your call back number if message was left on voicemail!
Austin AK2US 7/2/03 2112 EDT

## Slide 18: ARL Numbered Texts Purpose & How Counted
ARL Numbered Texts replace common phrases in message body text (i.e., Happy Birthday, Greetings by amateur radio, etc.)
Use of ARL texts reduce total message word count – faster and more consistent transmission of text
Translated before delivery of message to addressee

## Slide 19: ARL Numbered Texts Purpose & How Counted
ARL text numbers are always spelled-out in words (i.e., ARL SEVEN or ARL FORTY SIX)
Message word count (check) is written as “ARL #” (e.g., ARL 4 or ARL 15) to alert operators that message includes at least one ARL numbered text
Use ARL prefix in count, e.g. ARL 15

## Slide 20: ARL Numbered Radiograms

## Slide 21: ARL Numbered Texts (Example)
ARL FIFTY = Greetings by amateur radio
ARL FIFTY SIX = Congratulations on your ____, a most worthy and deserved achievement
ARL SIXTY NINE = Welcome to the ____. We are glad to have you with us and hope you will enjoy the fun and fellowship of the organization

## Slide 22: ARL Numbered Texts (Example)
Actual Message: Greetings by Amateur Radio. Congratulations on your new call sign, a most worthy and deserved achievement. Welcome to the amateur radio world. We are glad to have you with us and hope you will enjoy the fun and fellowship of the organization

## Slide 23: Net Etiquette
When checking in
  Say “Net Control” then unkey
  give your call sign phonetically
  wait to be acknowledged by Net Control
  list your traffic (or say “no traffic” or QRU)
  say if you can handle any of the traffic listed
  remain on-frequency unless excused by net control

## Slide 24: Sending a Message (Phone)
don’t say labels such as “priority” and “station of origin”
read at about half of normal reading speed
say “Break” and unkey immediately before and after the text
if the text is long, unkey during the text to allow recipient to ask for fills

## Slide 25: Sending a Message (Phone)
Use prowords:
  “I spell”
  “figures”
  “initial”
  “direction”
  “operator’s note” (usually after the message)

## Slide 26: Sending a Message (Phone)
Other prowords:
  “over”
  “out”
  “clear”
  “roger” (or QSL)
  “affirmative”
  “negative”
  “say again”

## Slide 27: Sending a Message (Phone)
when spelling, use ITU phonetics
say “niner” for the number nine
at the end of the message:
  say “End, no more”, or “End, one more”, etc.
  say your call sign

## Slide 28: Receiving a Message (Phone)
to ask for “fills”, say:
  “please say again, word after …”
  “please say again, word before …”
  “please say again, all between …”
  “please confirm …”
compare the check to the number of words you copied
once you have copied the message successfully, say “I roger (or QSL) your message number …”

## Slide 29: Notes on Message Text
NEVER “correct” the text of a message.
If, for some reason, you feel the text was received incorrectly, ask for a fill.
If the fill is the same as the original copy, but you still feel it is incorrect, NEVER “correct” the text yourself. Use the text as sent to you.
It is OK to query back to the originator.

## Slide 30: Book Traffic
Messages with the same (common) text
Have different recipients/addressees
Think of them as Microsoft Word “Mail Merge” documents
Example is ARL Numbered Radiogram we saw before.

## Slide 31: Book Traffic
When listing them on a net, say you have book traffic
NCS should send book traffic to another frequency
Send common text first
Send recipients/addresses last

## Slide 32: How to Deliver an NTS Message
Deliver via telephone, e-mail, US mail, CW or digital modes.
Okay to leave on voicemail IF you are comfortable you reached the right person.
Send radiogram via US Mail if cannot reach recipient by phone or e-mail.
Service originating station to inform if unable to deliver message or if they requested confirmation (via HX codes).

## Slide 33: How to Deliver an NTS Message
If delivering by phone, identify yourself as a ham radio operator and state you have a radiogram from ______
Don’t say “X-ray” or “Query” to message recipient – deliver in plain English
Expand ARL radiograms when you deliver message – do not use ARL codes

## Slide 34: Actual Traffic Net (4:21)

## Slide 35: Traffic Nets
WPA 2 meter traffic net
  147.270 + pl 131.8 every Friday at 8:30 pm
WPA Section Traffic Net
  3.983 LSB daily (times vary with season)
Interstate Sideband Net
  3.985 LSB daily at 0100 UTC

## Slide 36: Sending Traffic via Digital Modes
Tigertonics SignaLinkTM USB Sound Card

## Slide 37: FLDIGI/FLMSG
Most popular way to send digital traffic
Free software from W1HKJ Dave Freese
  http://www.w1hkj.com
“Field Friendly”
  Deployment is quick and easy

## Slide 38: FLMSG
ARRL Radiogram form is integrated into FLMSG
FLDIGI must be running to send traffic from FLMSG
  Can have FLDIGI minimized

## Slide 39: FLMSG DEMO

## Slide 40: Q/A on ARRL Radiograms
Questions on ARRL Radiograms?
If not – leaving ARRL Radiograms
Going to FEMA ICS-213
  Used by ACS/RACES and local EMAs
  Plain language form
    Much simpler/plainer than Radiograms

## Slide 41: FEMA ICS-213 FORM

## Slide 42: FEMA ICS-213 FORM

## Slide 43: FEMA ICS-213 FORM

## Slide 44: FLMSG
ICS-213 form is integrated into FLMSG
FLDIGI must be running to send traffic from FLMSG
  Can have FLDIGI minimized

## Slide 45: FLMSG DEMO

## Slide 46: Questions on ICS-213?

## Slide 47
FINAL Q & A
THANK YOU FOR YOUR PARTICIPATION!
73 de NU3Q